## Slide 1: BULDIBUYO PROJECT - GCI MINING GROUP SAC
BULDIBUYO – PATAZ
LA LIBERTAD
2024

## Slide 2: LOCATION AND ACCESS TO THE PROJECT
The Buldibuyo Project covers 1210 Has. It is located in the district of Buldibuyo, province of Pataz, department of La Libertad.
The area is accessible either by land or by air, It´s an 815 km land route itinerary from the city of LIMA–CHIMBOTE–SIHUAS–TAYABAMBA-BULDIBUYO aproximately. From this last town, it continues by road towards Huaylillas and before crossing the bridge (Huascacocha river), there is a turn off leading to Tarabamba Hydroeletric Power Plant. From there, it follows a 3 Km. truck trail until it reaches the project site.
The air travel is made by small commercial plane from LIMA to the PIAS airport, from there it continues by an unpaved road. There is also an airport in Tayabamba.

## Slide 3: PROJECT ACCESS TABLE
Access to Los Hornos project
In order to get to the study area, the following itinerary was used:
By land
Lima – Chimbote – Sihuas – Tayabamba – Buldibuyo (19 hours)
Air travel
Lima – Pias airport (Aircraft 1 hour)
Pias airport – Buldibuyo (3 hours and 30 minutes by land)

## Slide 4: VIEW OF THE PROJECT
CAMPAMENTOS
MINA
PLANTA
EXPLORACION

## Slide 5: MINING PROPERTIES
CODE | CONCESSION | HOLDER | HA | DISTRICT | PROV. | DEPT.
15008764X01 | PATRICIA | GCI MINIG GROUP S.A.C. | 510 | BULDIBUYO | PATAZ | LA LIBERTAD
10080194 | MARIA ANGOLA 2 | GCI MINING GROUP S.A.C. | 730 | BULDIBUYO | PATAZ | LA LIBERTAD
 |  | TOTAL | 1240 |  |  | 
The project consists of 2 mining properties all contiguous in the district of Buldibuyo, in the province of Pataz, Department of La Libertad.

## Slide 6: CADASTRAL MAP

## Slide 7: REFERENCE WHIT OTHERS PROJECTS

## Slide 8: LOCATION OF ANOMALIES

## Slide 9: GEOLOGY
The Project is located within intrusive granitoid rocks known as Batolito of Pataz (Paleozoic age) that are sensed by phyllite schist, slates and metavolcanics of the Maran Complex (Precambrian age). The Batolito of Pataz extends as a belt of Northwest course and width of 1 to 3 Km. Between Vijus in the north and Buldibuyo to the south.
The project is hosted by granitoid rocks from the Batolito of Pataz (microdiorite granodiorite and granite). Its consists of quartz veins with lenticular concentrations of sulfides mainly pyrite and free gold contents. The ore concentration is presented in the form of a mineralized body (Ore Shoot) controlled by structures of the Cimoid Loop type. The main ore is the gold pyrite (fine-grained pyrite microfacted); arsenopyrite galena marmatita is also found in a lesser proportion ; it is also possible to find free gold in the sacaraoid quartz.
Milky quartz is the main gangue mineral of, along with a tiny amount of calcite and kaolin. The wall rocks of the quartz veins adjacent to the areas where the economic concentrations of gold material are present due to hydrothermal alteration are silicified, sericitized and chloritized. These alterations are absent where the vein lacks mineralized filler.

## Slide 10: HISTORICAL PRODUCTION OF MINES IN THE BATOLITO DE PATAZ

## Slide 11
LONGITUDINAL SECTION WITH HISTORICAL DATA UNDERGROUND SAMPLING, POWER (M) AND LAW (GT / AU)
Posible zona de
Diseminado en intrusivos
o Sistema de Vetas
13.27 m@5.09 gt/Au
8 m@15.89 gt/Au
22.6m@9.3gt/Au
24.5m@3.8gt/Au
8.5m@10.2gt/Au
22.7m@3 gt/Au
9.8m@0.7gt/Au
71.2m@2.38gt/Au
9.3m@11,1gt/Au
7m@5.6gt/Au
9.8m@6.9gt/Au
53.2m@2.9gt/Au
11.75 m@6.47 gt/Au
27.5m@4.7 gt/Au
10.1m@6.5gt/Au
16.6m@14.2gt/Au
Here is shown the historical data with its average power and grade and the possible zone of Disseminated in Intrusive or a Vein system with a grade of 0.5 to 84 gr / tn and a power of 0.25 to 2.36m but with a continuous distribution and consistent throughout the area.

## Slide 12
Los datos obtenidos son parte los datos históricos de la sección longitudinal veta patricia
BULDIBUYO GOLD LOCATION OF SAMPLES IN CROSS SECTION

## Slide 13: ORE BELT
PROYECTO BULDIBUYO

## Slide 14: PROJECT GEOLOGICAL MAP

## Slide 15: PROJECT STRUCTURES

## Slide 16: DRILLING LOCATION

## Slide 17: SONDAJE REALIZADO

## Slide 18: STRUCTURAL LINEAMENTS

## Slide 19: ECONOMIC GEOLOGY
Orogeny originated two stages of intrusion, by magmatic differentiation, the first instrusions were of an intermediate composition as well as the diorites and those that predominate in the batholith, the later sequences were getting more acidic such as tonalites, granodiorites and monzonites quartz which together represent a 2nd. The magmatic pulsation is what has given rise to the auriferous veins in the batholith.
Hydrothermal mineralization of pyrite-chalcopyrite-gold association occurs in veins hosted in intrusive rocks of the batholith. The most persistent structures (up to 900 meters) as the Patricia vein, shows an N-S orientation, dipping 35° E.
At Patricia prospect, 3 potential areas of economic interest are presented; area of the North Patricia vein (where mining exploration is currently taking place), South Patricia and San Juan vein, and the third would be Las Ruinas vein. There are also other minor mineralized areas such as The Horno zone, San Pedro vein, la Colorada, los Pilancones, el Murcielago and Pishgon which is at the boundary of the claim.

## Slide 20
PROPERTY OUTCROP VEINS

## Slide 21
San Juan vein outcroppping on the south of Don Julio’s Fault. We observed a milky quartz crest of 1 m of power.

## Slide 22: GEOPHYSICAL CONCLUSIONS AND RECOMMENDATIONS
VDG of Peru S.A.C. completed a second terrestrial geophysics campaign in October 2008. The applied geophysical methods were the study of magnetometry and induced polarization. The objective of the geophysical campaign at Los Hornos gold project was to determine the extent of the anomaly detected in the first geophysical campaign, related to a possible Cu-Au porphyry in depth.
The geophysical results allow us to conclude the following:
1. The resistivity delineates values of moderate-high resistivities (<1,600 Ohm * m) from the surface to 100-150 meters in depth, corresponding to alteration zones or lithological contacts; and higher resistivity values (> 2,000 Ohm * m) at a greater depth.
2. Chargeability results match between the two campaigns, confirming a weak anomaly (IP-1) at an approximate depth of 200 meters. The IP-1 anomaly correlates with high values of depth resistivity.
3. The anomaly IP-1 outcrops to the east of the 1500N line, in the Huascacocha ravine.
The limits of the anomaly have been delineated in the sections and on the interpretation map.

## Slide 23
EXPLORATION AREA

## Slide 24
GEOPHYSICAL SECTIONS

## Slide 25
GEOPHYSICAL SECTIONS

## Slide 26
MINA
NIVEL 2700 TUNEL WILDER

## Slide 27
Being the deposit of filonean type with medium to low power and sub-horizontal dip, it was not easy to select the exploitation method that best suits these and other requirements, choosing as a method of mining the “chamber with temporary pillars”, the same one that is done initially opening chambers alternately and ascending in the direction of the stope with a minimum section of 3 mt in width. Once the cutting of a chamber has been completed, we proceed to the aspiration, sweeping and washing of the pit, thus remaining ready for the filling stage. In a second stage of mining, the pillars are exploited and filled.
Due to the multiple fracturing of the mineralized structure, special care is taken in the design of the drill pattern and the quantity of explosive, having as a control the indices of drilling factor and blasting, whose values are of 3.5 m/m3 and 0.90 kg/m3 respectively. In order to control the blasting, measurements of the ground vibrations are made with an automatic digital seismograph. Hence the incidence in the use of lower power explosives with water dampers in each drill, which are manufactured in the mine.
MINE

## Slide 28
After the blasting is proceeded to ensure the pit, depending on the competence of the hanging wall, wood frames, safety props, anchor bolts fixed with resin and/or jacks (tool), hydropneumatic recoverable are used as support elements , these last ones allow to lower the costs, protect the environment and ecology by reducing the consumption of wood.
The very fine particles of gold ore that are found in the interstices of the stope or that are floating, are recovered with a last generation new system of suction of South African origin, which offers interesting results in the recovery of fines that the sweep will not be able to capture.
To restore the balance of the rock mass and control the subsidence, cemented hydraulic filling is used, filling the space voids created by the exploitation. This filling has as raw material a mixture of alluvial sands with cement, which once deposited in the pit, reaches a 0.8 kg/cm2 resistance to the uniaxial compression.

## Slide 29
GENERAL MAP OF THE PROJECT AREA
BARLEY HILL
BARLEY HILL

## Slide 30
RESOURCES

## Slide 31
PATRICIA VEIN |  |  |  | 
INDICATED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | GRADE | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
ONE | 1.08 | 11,418 | 11.25 | 4,130
TOTAL |  | 11,418 | 11.25 | 4,130
INFERRED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | GRADE | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
TWO | 1.08 | 19,776 | 10.22 | 6,499
THREE | 1.08 | 19,897 | 10.22 | 6,538
TOTAL |  | 39,673 | 10.22 | 13,037
GRAND TOTAL |  | 51,091 | 10.45 | 17,167
PATRICIA VEIN

## Slide 32
PATRICIA DOS VEIN |  |  |  | 
INDICATED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | GRADE | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
ONE | 1.00 | 2,621 | 8.35 | 704
TOTAL |  | 2,621 | 8.35 | 704
GRAND TOTAL |  | 2,621 | 8.35 | 704
PATRICIA DOS VEIN

## Slide 33
SAN JUAN VEIN |  |  |  | 
INDICATED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | GRADE | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
ONE | 1.00 | 8,320 | 10.50 | 2,809
TWO | 1.00 | 13,620 | 10.50 | 4,598
TOTAL |  | 21,940 | 10.50 | 7,407
INFERRED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | GRADE | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
THREE | 1.00 | 15,459 | 12.05 | 5,990
TOTAL | 1.00 | 15,459 | 12.05 | 5,990
GRAND TOTAL |  | 37,399 | 11.14 | 13,397
SAN JUAN VEIN

## Slide 34
SAN JUAN DOS VEIN |  |  |  | 
INDICATED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | PURITY | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
ONE | 1.00 | 1,663 | 12.50 | 668
TWO | 1.00 | 5,783 | 12.50 | 2,324
TOTAL |  | 7,445 | 12.50 | 2,992
INFERRED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | PURITY | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
THREE | 1.00 | 5,783 | 12.50 | 2,324
TOTAL |  | 5,783 | 12.50 | 2,324
GRAND TOTAL |  | 13,228 | 12.50 | 5,317
SAN JUAN DOS VEIN

## Slide 35
LOS HORNOS VEIN |  |  |  | 
INFERRED RESOURCES |  |  |  | 
BLOCK | POT. | TONNAGE | PURITY | FINE CONTENT
 | mts. | ton. | gr Au./ ton. | ounces
 | 2.45 | 152880 | 11.00 | 54073.31
TOTAL |  | 152880 | 11.00 | 54073.31
LOS HORNOS VEIN

## Slide 36
CLASSIFICATION BY VEINS |  |  |  | 
VEIN | RESOURCES | TONS | GRADE | OUNCES
 |  | ton. | gr. Au./ ton. | Au.
PATRICIA | INDICATED | 11,418 | 11.25 | 4,130
 | INFERRED | 39,673 | 10.22 | 13,037
SAN JUAN | INDICATED | 21,940 | 10.50 | 7,407
 | INFERRED | 15,459 | 12.05 | 5,990
PATRICIA DOS | INDICATED | 2,621 | 8.35 | 704
SAN JUAN DOS | INDICATED | 7,445 | 12.50 | 2,992
 | INFERRED | 5,783 | 12.50 | 2,324
LOS HORNOS | INFERRED | 152,880 | 11.00 | 54073
 | TOTAL | 257,218 | 10.96 | 90,648

## Slide 37
MINERAL RESOURCES |  |  | 
ZONES | TONS | GRADE | OUNCES
 | ton. | gr. Au./ ton. | Au.
INSIDE MINE | 257,218 | 10.96 | 90,648
STOCKWORK | 40,000,000 | 1.5 | 1,929,043
TOTAL | 40,257,218 | 1.56 | 2,019.691

## Slide 38
The selective cut and fill method is necessary to achieve the lowest dilution in the ore exploitation as well as the minimum loss of fines due to the blasting in the stopes in order to achieve the highest profit as a result of the high grade ore extration, especially the exploitation of high value ores in the market.
A 1.20m x 2.10m “sill drive” bridge is developed with the length of the block and 2.50 meters above the back of the base drift, keeping the structure of the vein on the hanging wall. The waste and vein ore will be detonated independently under strict geological control during exploitation.
Before detonating the vein, a steel plate covered with 4mm wide protection will be placed on the pit floor so as to reduce the loss of ore fines. The soil will be swept and finally placed in bags for transport to the surface.
The detonated ore is laoded by hand in wheelbarrows and hauled to the ore pass. The ore passes are connected to each vertical lift, so that one of its sides will be built with wooden walls as the exploitation progresses upwards.
EXPLOITATION METHOD
SELECTIVE CUT AND FILL EXPLOITATION METHOD

## Slide 39
Stope prepared for production Longitudinal section of the vein
Continuous stopes prepared for production Longitudinal section of the vein.

## Slide 40
When the ore withdrawal is finished, the waste is detonated to create a new soil. The soil is then leveled, the barrier replaced and the ore is detonated again. Each lifting is 1.8 meters high.
The amount of waste required to fill the void space, that each lift caused and provide a floor to work each subsequent lift, will vary with the thickness of the vein, but as a general rule, approximately twice the thickness of the grain must be drilled and detonated.
The steps are repeated until the block is mined to its upper limit. The ore will run from the hopper to the tractor and will be hauled to an ore pass on a level platform. A hopper covered by concrete steel will take the mineral to the storage container in the lower level so as to be transported to the plant in 25 ton trucks.
A mineral storage shed with sufficient capacity to sustain a production of weeks will be built on the lower level as protection against road interruptions. This shed will be constructed first to provide safe and covered storage while the hopper/recipient installation is constructed.

## Slide 41
Stope mining
Sections of the sequence of production of stopes

## Slide 42: VIEW OF EL CURA AREA

## Slide 43: 30 TON/DAY CARBON IN PULP PLANT FOR GOLD PROCESSING

## Slide 44: PANORAMIC VIEW

## Slide 45: COARSE HOPPER*
1.- CRUSHED SECTION
The ore is extracted from the mine on mining trucks (U-35) to a coarse hopper.
The coarse hopper has a capacity of 30 MT. It has a metal gate of mechanical handling, with a ½” grill, it goes straight to a jaw crusher.

## Slide 46: CONVEYOR BELT
CONVEYOR BELT.
The ore is transported after the jaw crusher to the fines hopper, through a belt with electric engine.

## Slide 47: FINES HOPPER
FINES HOPPER
It is made of metal structure of 10’ diameter x 6’ height, with a 15 MT storage capacity. Hopper with support, at the bottom it has a conveyor belt that goes to the mill.

## Slide 48: ROLLER CRUSHER
SECONDARY CRUSHING.
The transported ore arrives first at the vibrating sieve, with a ½” grill.
The smaller volume ore passes directly to the fines hopper, the thick ones goes to the roller crusher and then falls into the fines hopper.

## Slide 49: ENERGY DISTRIBUTION SYSTEM
ELECTRICAL DISTRIBUTION.
The 440 and 220V electrical cables are distributed after the main board in “cable ducts” to the secondary control boards of each section.

## Slide 50: BALL MILL 4” x 4”
GRINDING.
After the fines hopper, the ore is transported through a conveyor belt with discharge chut to the ball mill The mill inside has steel balls of different diameters to grind the ore to a -200 mesh, then the ground ore passes through a gravimetric concentrator where the grinding mesh can be measured and it goes to a helical classifier, the classifier with an inclination of +10° has the property of capturing the greater grain concentrate from the required mesh and return it to the mill. The fine concentrate diluted with cyanide solution (Na, Cn, H2O) goes to the SRL Galigher pump, through a 2 ½” pipe. The SRL pump transfers the solution with the concentrate to a Cyclone and it distributes to the agitator tank, in the grinding process there is a lime doser that is graduated as required for the mill.,

## Slide 51: GALIGHER PUMP
SRL PUMP.
The SRL pump transfers the solution, through a 2” diameter pipe to the cyclone, at this grinding section and SRL pump, there is a remote control board that controls this area engines.

## Slide 52: AGITATOR AND CYCLONE TANK
AGITATOR TANK.
The cyclone distributes the “rich” solution with the fine concentrate to the first agitator tank (“super” agitator), and the coarse concentrate passes to a thickener and it returns to the grinding, in the tank A-1 the solution has a 48 hour agitation process and then moves on to the following tanks. In this area there is a Barren solution tank, this solution is transferred from the tailings through a 2” pipe by a 20 HP KSB pump. From 1700 Rpm. This solution contains reagents that are used again in the grinding so as to lower the process costs.

## Slide 53: CYANIDATION TANKS
AGITATOR TANKS.
The tanks have a continuous agitation process, after the solution passes through tank A-1, the solution goes to tank A-2 and after 24 hours of agitation it goes to tank A-3. After this agitation process the solution goes to the CIP tanks. In this area, there is a reagent doser (Cyanide) whose gravity goes to the grinding section for the fines capture.

## Slide 54: TANKS FOR CIP
ABSORPTION TANKS (WITH ACTIVATED CARBON) CIP.
After tank A-3, agitation process, this enriched solution passes to the absorption tank CIP-1, which contains activated carbon, gradually after the agitation process where the fine is absorbed by the coal, the less “enriched” solution passes to CIP-2 and successively to CIP-3. The 03 tanks contain activated carbon and are “harvested” after being enriched, with previous analysis of the coal and solution. In this area there is an air compressor (blower) that is in charge of oxygenating all the agitation tanks.

## Slide 55: CONCENTRATOR PLANT FLOWCHART

## Slide 56: HYDROELECTRIC POWER PLANT OF TARABAMBA LOCATED 2.5 KM FROM THE PROJECT

## Slide 57
PHOTO GALLERY

## Slide 58
MINE

## Slide 59
PROJECT FACILITIES

## Slide 60: CAMPS AT THE PROJECT SITE

## Slide 61
DISSEMINATED POTENTIAL - EL CURA AREA

## Slide 62
M-284 15.9 ppm
M-752 14.25 ppm
M- 587 1.83 ppm
CHANNEL SAMPLING– Zona EL Cura
50 meters, 0.1 gr/t Au up to 15.9 gr/t Au
SE
NW
STOCKWORK
POTENCIAL DISEMINADOS ZONA EL CURA