## Slide 1: LOS HORNOS & EL CURA PROJECT
Auriferous disseminated mineralization- Buldibuyo
2024

## Slide 2: LOCATION AND ACCESSIBILITY
Los Hornos project is located in the district of Buldibuyo, province of Pataz, La Libertad Region.
In order to the study area, the following itinerary was used:
By land
Lima – Chimbote – Sihuas – Tayabamba – Buldibuyo (19 hours)
Air travel
Lima – Pias airport (Aircraft 1 hour)
Pias airport – Buldibuyo (3 hours 30 minutes by land)

## Slide 3: LOCATION AND ACCESSIBILITY

## Slide 4: Cadastral Plan
CODE | CONCESSION | HOLDER | HA | DISTRICT | PROV. | DEPT.
15008764X01 | PATRICIA | GCI MINIG GROUP S.A.C. | 510 | BULDIBUYO | PATAZ | LA LIBERTAD
10080194 | MARIA ANGOLA 2 | GCI MINING GROUP S.A.C. | 730 | BULDIBUYO | PATAZ | LA LIBERTAD
 |  | TOTAL | 1240 |  |  | 
The Project consists of 2 contiguous mining properties in the district of Buldibuyo.

## Slide 5: Regional Geology - Metallogenetic Belts
Modificado de INGEMMET,
Orogenic deposits of Au-Pb-Zn-Cu
of the Carboniferous-Permico
Deposits MTV type of Pb-Zn of the Eocene-Miocene
Au deposits in metasedimentary
Deposits of Au-Cu-Pb-Zn
in Eocene intrusives

## Slide 6: Regional geology
The Pataz batholith is historically characterized by the presence of mesothermal vein gold deposits , also called Orogenic Gold. It has been exploited since the Incas period and for the last 100 years. More than 16 underground mines distributed between Pataz, Parcoy and Buldibuyo, have produced 6 million gold ore ounces and it is estimated that its ore reserves would reach up to 40 million considering the entire belt(Haeberlin Y., 2002).
The Pataz batholith is an intrusive body, located in a regional fault with a directional trend NNO-SSE parallel and along the Marañón valley, presenting itself as a corridor or structural via of mineralization, covering dimensions of 160 km. of variable length and 1 - 3 km. in width, emplaced in the oriental flanks of the Eastern mountain range, this regional fault would have controlled later the formation of the vein systems. (Schreiber et al., 1989, Haeberlin et al., 2002, cited in Haeberlin Y., 2002).
Los Hornos and El Cura prospect is immersed in the Pataz - Parcoy – Buldibuyo metallotect auriferous at its southern end.
Datings of 40Ar / 39Ar in biotites of monzogranite rocks and granodiorites of the Pataz batholith, determined ages of 329.2 ± 1.4 and 328.1 ± 1.2 Ma. Respectively (Haeberlin, 2002), ages that belong to the Mississippian of the Carboniferous.

## Slide 7: Regional Geology Los Hornos
A
B

## Slide 8: Regional geology – Profile
Modificado de, Arones

## Slide 9: Regional geology – Stratigraphic column
Modificado de, Haeberlyn

## Slide 10: Local Geology
The area of interest of the prospect is located in Los Hornos & El Cura area presenting a structural compartment, limited by major fault systems, to the west is the fault of the Huascacocha river and to the east are Los Hornos fault and the Huiro Huiro river fault.
In the Eastern side , on Alto Cebada Hill, the Jhire mine is located, In that deposit, the main fault systems are presented, such as the Murciélago fault, the María Esther fault and Don Julio fault.
The mineralization at Jhire mine is associated with large regional N-S striking faults (shear zones), represented by veins, located on the left side of the Huascacocha river, in strike N0 ° -10 ° W, formed by vein systems of fissure fillings, denominated Patricia and San Juan vein with mineralizations of (quartz 70%, gray silica 5%, sulfides like pyrite, sphalerite, galena and native gold).
In the area of Los Hornos, Vdg del Perú s.a.c. completed a second terrestrial geophysics campaign in October 2008. the applied geophysical methods were the study of magnetometry and induced polarization.
Most of the local geology information of Los Hornos prospect, comes from the work carried out by Merendom Peru mining company and the thesis of Yuri Arones.

## Slide 11: Local Geology
Panoramic view of Los Hornos and the batholith of Pataz - Buldibuyo. Looking North - East.

## Slide 12: Local Geology - Lithology
Modificado de Y. Arones

## Slide 13: Local Geology - Structural
Modificado de Y. Arones

## Slide 15: Lithology
Los Hornos prospect(Los Hornos & El Cura) is comprised of quartz diorites, tonalites, granodiorites, granites, andesitic dikes and aplitic dikes.
Numerous plutonic intrusions occurred in the Pataz Batholith, particularly at Los Hornos prospect, being the oldest unit, the granitic or sienogranite emplacements, occured by granodiorite intrusions and laterly intrusions of tonalites nature and dioritic stock.
The macroscopic description of rock outcrops in the field works, are corroborated by studies of petromineragraphy, and streckeisen diagram.
The faults are associated with andesitic and aplitic dikes.
Other intrusive outcrops near Los Hornos, is located on the Alto Cebada hill, where monzonitic stock outcrops, a probable magmatic activity Late Cretaceous (80-65 Ma.), which is not related to the auriferous mineralization of the Pataz batholith (314-312 Ma.), which are commonly found in northern Marsa Mine (Haeberlin, 2003).

## Slide 16: Lithology

## Slide 17: Lithology

## Slide 18: Lithology

## Slide 19
Sample 569 - 1.12 g Au / t

## Slide 20: Litology

## Slide 21: Hydrothermal alterations
The superficial manifestations of the alteration and main hydrothermal mineralization are presented in a conspicuously way and in form of a penetrative type in Los Hornos zone (hot zone), presenting a pervasive phyllic hydrothermal alteration (associations of minerals sericite, quartz, muscovite, corundum and carbonates, with sericitic halos along the contiguous edges of the veins and quartz veinlets and in fractures, with plagioclase crystals replaced by sericite.
The strong phyllic alteration scales towards areas with moderate phyllic alteration, with a presence of argillic alteration with clay minerals : kaolinite and montmorillonite as a result of plagioclases alteration , in levels and / or intermediate heights of Los Hornos area. The phyllic and siliceous alterations would be lmainly related to granitic type and porphyritic sienogranites magma.

## Slide 22: Hydrothermal alterations
Propyilitic alteration of mesothermal environments occurs in dioritic intrusions that indicate peripheral vertical zones to the hydrothermal system centered in Los Hornos zone, with mineralogical assemblages of chlorite, epidotes and carbonates (calcite veins), the presence of hornblende altering to chlorites, calcite and epidotes; the crystals of plagioclase and hornblende are altered to calcite. The biotites are altered to chlorites.
Potassium alterations occur punctually, with the presence of secondary muscovite in tonalites and diorites; also in some superficial outcrops occurs scarce contents to traces of pyrophyllite, (Ocharán G., 2006.)

## Slide 23: Hydrothermal alterations
Photo looking North

## Slide 24: Structural
Los Hornos zone presents in its surface geological manifestations, a very peculiar structural behavior, which geometrically and structurally shapes the probability of a deposit in depth, this has been called "structural compartment".
Los Hornos structural compartment presents superficially domains and / or polydirectional structural tendencies of fracturing systems towards its interior, presenting areas of shear (shear zone), crackings (crackle ), and in a very local way, breccia zones; These crackle-breach fracture systems are open at the district level to the northwest of the Patricia concession.
The projection of 1564 fracture data from structural stations throughout the El Cura area in a rosette diagram, determines polydirectional distributions of fractures, in fracture planes with dips between 0 ° to 90 °. The polydirectional fractures present a network entrapment of polydirectional quartz veinlets in depth.

## Slide 25: Structural
The structural control and / or degree of fracturing at Los Hornos prospect is the main factor in the depth mineralization trap.
Major fault systems with abrupt to gradual inflections, such as the fault of the Huascacocha River, have generated areas of structural control with opening of local spaces or extensions that have contributed to the movement of hydrothermal fluids (structural permeability); they also present local compression zones that have restricted the passage of hydrothermal fluids, in their different stages of mineralization.
The analysis of all the vein systems (> 5cm wide) and quartz veinlets (<5cm to 1cm wide) from Los Hornos area, determined poly-directional tendencies of the mineralization systems (cross veinlets).

## Slide 26: Structural

## Slide 27: Structural

## Slide 28: Structural

## Slide 29
SAMPLE M-587 : 1.83 g Au/t

## Slide 30
SAMPLE M-752 : 14.25 g Au/t

## Slide 31
SAMPLE M-284 :15.90 g Au/t

## Slide 32
SAMPLE M-753, M7-54 :1.48 g Au/t

## Slide 33
SAMPLE M-728 : 1.275 g Au/t

## Slide 35
GEOPHYSICAL LINE 8500N AND EXPLORATION DRILLING
LH07-05
LH07-05

## Slide 36
LINE GEOLOGICAL SECTION 8500N

## Slide 37: Structural

## Slide 38: Mineralization
Gold mineralization events occur mainly in areas of higher cracking with moderate to strong phyllic alteration, through a structural control related to systems of millimetric veins and veinlets to centimetric polydirectional quartz with fillings of hematite, goethite and limonites oxides in fractures together with pyrite in veins and in a fine interstitial dissemination, with low content of sulfides as galena, sphalerite, chalcopyrite, arsenopyrite, pyrrhotite and coveline replacing chalcopyrite, with textures of replacements and comb structure.
The formation of hematite and goethite veinlets occurs in replacements of pyrite and magnetite mineralizations. Some phases of pyrite is associated with free gold, also occurring locally in auto-breach zones such as a fine gold dissemination, trapped in the intersecting quartz veinlets

## Slide 39: Mineralization
Electron microscopy studies of surface samples determined the presence of free gold, not greater than 60 microns associated with quartz veinlets, they appear in the form of inclusions in the hematite and goethite, which replace the pyrite of which their geoforms remain (Ocharán G, 2006).
They also present inclusions of ancient chalcopyrites with fine dissemination that have been replaced by covelina (supergene alteration); with the presence of disseminated gold mineralization, the pyrite sizes do not exceed 20 microns.

## Slide 40: Mineralization Control
The study area mainly presents a structural control of the mineralization represented by the intercrossing of quartz veins and veinlets and the density in their fractures.
The planes of density of fractures and penetrative hydrothermal alterations, focus on the permeability of the hydrothermal zones, with the presence of polydirectional quartz veins and veinlets (crossing of veinlets) with free gold, Fe oxides and sulfides.

## Slide 41: Mineralization Control
A control of the mineralization by hydrothermal alterations is presented, being the Sericite, contiguous to the veins and quartz veinlets the one that presents greater mineralization. Mineralogical control is also presented in veins and veinlets of auriferous quartz with presence of fine pyrite, galena and sphalerite.
In smaller proportion, a lithological control due to the compositional differences of the rocks that appear in their different locations mark their difference, being the dioritic and tonalitic rocks the ones that presents greater mineralization than the granitic rocks, with the presumption that the tonalitic and dioritic sites could be responsible for the mineralization in the area.

## Slide 42: Mineralization Control
Los Hornos. Quartz veins with limonites, cutting granodiorites, partially brecciated

## Slide 43: Mineralization Control
Los Hornos. Mining works in sericitic alteration and breccia zone in granodiorite.

## Slide 44: Mineralization Control

## Slide 45: Sampling
We collected and recorded 173 sediment runoff samples, 1st, 2nd. and 3rd order, collected along the streams, from the study area
The collection and registration of information on 271 rock samples was carried out for its geochemical analysis. Two types of geochemical sampling were carried out, the first geochemical sampling consisted of the collection of 129 samples of outcropping orientation (rock chips), and the second type of geochemical sampling consisted of the collection of 142 systematic samples in mesh (rock chips), which was 100mx25m between sample and sample.
The collection of 14 samples of undistorted and representative rocks of each lithological unit of the study area was carried out and the corresponding information was recorded, for its geochemical analysis by total rock, the size of each rock collected sample was up to 2.5 kg.
A total of 15 samples of rock outcrops and hydrothermal alterations were collected and recorded, for studies of petro-mineragraphy and electronic microscopy, the samples collected in the study area field, are representative of each lithological unit, and were sent to the laboratory of Dr. Gladys Ocharán, (2006).
For the geochemical analyzes, the samples were sent to the BSI Inspectorate Griffith and ALS CHEMEX laboratories, and were analyzed by gold using the analytical package Fire Assay, Atomic Absorption Au 30g., Gravimetric method (AA24 and GRA21) and multielement analysis (ME-). ICP41) previous digestion by aqua regia .

## Slide 46: Geochemistry
Out of the 271 rock samples, mainly in Los Hornos zone, the results of the primary geochemical dispersion, in gold and multielements, show maximum and minimum values.
In Au, a Background of 0.014ppm Au and Threshold 0.040ppm Au was determined, with a medium value of 0.13ppm Au and a mode of 0.006ppm Au.
The anomalous values in gold ≥0.040 ppm Au in rock samples are mainly concentrated in Los Hornos area, with an anomaly open to the northwest, which represents 32% of the total sample population; 29% of samples show a strong anomaly ≥ 0.066ppm Au, with a maximum value of 15,900ppm Au.

## Slide 47: Geochemistry
The Pearson correlation analysis of 271 rock samples determined positive correlations> 0.5 between the elements: As-Pb (0.72), Cu-Zn (0.62) that represent moderate positive correlations and Mn - Ba (0.57), Cu - Pb ( 0.54), Zn - Pb (0.51) that represent weak positive correlations.
A statistical analysis of the 173 sediment runoff samples results in Los Hornos zone indicated a maximum value of 6,480ppm Au and a minimum of 0.005ppm Au, determining a Background of 0.025ppm Au and a Threshold of 0.097 ppm Au and a mode of 0.010ppm Au.
The anomalous gold values of sediments ≥0.097 ppm Au, mainly surround Los Hornos zone, focusing the economic interest area of the deposit, among N 9'101,000 - N 9'101,700 and E 237,800 - E 238,800 coordinates . These gold results are the result of the erosion of the mineralization systems that occur in intrusive rocks in this area, which is the continuity of the Pataz batholith.

## Slide 48: Geochemistry
Pearson correlation chart

## Slide 49: Au and Cu anomalies
Plano anomalias Au
Plano anomalias Cu

## Slide 50: Conclusions
1) The confluence of the Huascacocha faults (N 335), and Huiro Huiro fault (N330) limit Los Hornos structural compartment; likewise, Los Hornos fault (N330) is found, those faults generate opening or extensional zones and the development of probable minor intrusions. Areas of intense cracking, shear areas (shear zone) and local breccias are presented.
2) Los Hornos, presents an extensive and pervasive hydrothermal alteration of quartz-sericite, grading to distal zones to propilitic alterations; presenting along the contiguous edges of the polydirectional quartz veins and veins sericitic with hematite, goethite, limonite, pyrite mineralizations in veins and in fine dissemination, with low content of sulfides such as galena, sphalerite, chalcopyrite, arsenopyrite , pirrotite and covellite.
3) The gold anomaly of sediments is focused on Los Hornos, towards the NW (Concesion Patricia), on intrusive rocks belonging to the Pataz batholith, that gold anomaly is open towards the NW. A statistical analysis of the results of the 173 sediment runoff samples, indicate maximum value of 6,480ppm Au and minimum of 0.005ppm Au, determining a Background of 0.025ppm Au and a Threshold of 0.097ppm Au and a mode of 0.010ppm Au .
4) Geochemical analyzes of the rock outcrops and subsequently a statistic of the results of 271 gold rock samples and multielements (Ag, Cu, Pb, Zn, Ba, As, Hg, Mo, Cd, Bi, Sb and Mn), present maximum values 15,900 ppm Au / 24.2ppm Ag / 400ppm Cu / 9110ppm Pb / 2580 ppm Zn / 100 ppm Ba / 10,000 ppm As / 23,800 ppm Hg / 31ppm Mo / 16.9 ppm Cd / 36 ppm Bi / 17ppm Sb / 1280 ppm Mn.

## Slide 51: Conclusions
5) The regional mineralogical zonation in the Pataz batholith can be divided into 2 zones: the northern zone, where the high-grade veinform systems are found in Au, Ag, As, Fe, Pb, Zn, ± Cu, ± Sb, ± Bi, -Te, -W and the southern zone with Au, Ag, Cu, Fe, Pb, Zn, ± As, ± Sb, + Te, where the gold would be found in vein-like systems and probable IRGS type systems, such as Los Hornos prospect.
6) The presence of free gold is associated with quartz veinlets, in the form of inclusions in hematite, goethite and limonite, which replace pyrite, accompanied by low sulfur content such as galena and sphalerite.
7) The mineralization style shows many similarities to IRGS deposit type (structural control of mineralization, hosted in stockwork). This possibility is unprecedented and atypical in the mining district of Pataz, due to the form of gold mineralization, mainly due to the dominant manifestation of the hydrothermal alteration to a great extent that is presented at Los Hornos prospect, which is what differentiates it from other areas, historically characterized by veins, of Pataz – Buldibuyo metallotect.
8) If the working hypothesis of an IRGS deposit is confirmed, we have examples of these deposits: Fort Knox with 0.46 gr / t Au and 2.4 million Au ounces; Dublin Gulch with 0.93 gr / t Au and 2 million ounces Au in Yukon - Alaska; Kindston with 4.5 million ounces in Australia, among others. Los Hornos prospect is very interesting and promising.
9) At Los Hornos, a potential of approximately 2 000kt / oz Au (40 'tm with 1.5gr Au / tm) is estimated.

## Slide 52: Recommendations
1) It is recommended to carry out a diamond drilling program to intersect, in depth, the mineralized bodies and their alteration, to recognize their geometry and contacts, as well as the continuity (increase) of auriferous mineralization. They are essential to know the ore potential at Los Hornos and have a first approximation to existing mineral resources.
2) To carry out an additional sampling of outcrops, taking into account trenches, pits and accesses or trails, in order to discover more rock in situ. These works would also allow to adjust and add more detail to the geological mapping (lithology, alterations, structural and mineralization).
3) The Pataz - Buldibuyo batholith is a "mature" (old) mining district, so we must emphasize this detail. In the same way, to break with the paradigm that you can only find veinform auriferous mineralization.
4) The proposed geological model (IRGS deposit type) here has been developed based on the various existing works compiled, information of personnel that have worked in the field and then analyzed; therefore, they should be tested and, where necessary, modified.

## Slide 53: Photos attached
View towards the West. Los Hornos Prospect

## Slide 54
TARGET TO STUDY
2019
EXPLORED AREA

## Slide 55: Photos attached
View towards the North. Los Hornos Prospect

## Slide 56: Photos attached
View towards the South. Los Hornos prospect

## Slide 57
PANORAMIC VIEW – ACCESS TO EL CURA

## Slide 58
PANORAMIC VIEW – ACCESS TO EL CURA

## Slide 59
PANORAMIC VIEW – ACCESS TO EL CURA